## Slide 1: DATA TRANSFERS IN ASSEMBLY
Sangram Kesari Ray <SHANKAR.RAY030@GMAIL.COM>

## Slide 2: DATA TRANSFER INSTRUCTION/S
OPERAND TYPES
  mnemonic
  mnemonic [dest]
  mnemonic [dest], [src]
  mnemonic [dest], [src1], [src2]

## Slide 3: MOV INSTRUCTION
MOV INSTRUCTION FORMATS
  MOV REGISTER, REGISTER //MOV EAX, EBX
  MOV MEMORY, REGISTER //MOV NUM1, EAX
  MOV REGISTER, MEMORY //MOV EAX, NUM1
  MOV MEMORY, VALUE //MOV NUM1, 10
  MOV REGISTER, VALUE //MOV EAX, 10

## Slide 4: MOVZX AND MOVSX INSTRUCTION
USE THEM WHEN COPYING FROM SMALLER SOURCE TO LARGE DESTINATIONS
  num1 byte 8 //8-bit src
  num2 byte -8 //8-bit src
  eax //32-bit dest
  mov eax, num1 //don’t do this, the register gets filled with incorrect
  movzx eax, num1 //copies a un-signed byte into 16-bit destination
  movsx eax, num2 //copies a signed byte into a 16-bit destination

## Slide 5: LAHF AND SAHF INSTRUCTION
LAHF //LOAD LOW-BYTE OF EFLAGS/RFLAGS (SIGN, ZERO, AUXILIARY, PARITY, CARRY) INTO AH REGISTER, AH IS THE HIGH-BYTE OF EAX
SAHF //LOAD AH INTO LOW-BYTE OF EFLAGS/RFLAGS
WHY BOTHER?
SUPPOSE WE WANT TO DO SOMETHING, LOOKING AT EFLAGS FOR 2 INSTRUCTIONS, BUT THIS EFLAGS KEEP CHANGING INSTRUCTION AFTER INSTRUCTION, WE NEED A WAY TO KEEP A TRACK OF THESE CHANGING EFLAGS.
EXECUTE INSTRUCTION #1 //ELFAGS CHANGED
SAVE EFLAGS INTO AH, STORE AH INTO NUM1
EXECUTE INSTRUCTION #2 //EFLAGS CHANGED
SAVE ELFAGS INTO AH, STORE AH INTO NUM2
IF NUM1 = NUM2
EXECUTE INSTRUCTION #3 // HOPE YOU GOT THE POINT, WHY USE LAHF AND SAHF INSTRUCTIONS?

## Slide 6: XCHG INSTRUCTION
ITS LIKE MOV BUT SWAPS THE VALUES
  MOV REGISTER, REGISTER //MOV EAX, EBX
  MOV MEMORY, REGISTER //MOV NUM1, EAX
  MOV REGISTER, MEMORY //MOV EAX, NUM1
  MOV MEMORY, VALUE //DOESN’T WORK
  MOV REGISTER, VALUE //DOESN’T WORK

## Slide 7: EFFECTIVE ADDRESSING
ACCESSING ELEMENTS IN AN ARRY //CONTIGUOUS MEMORY LOCATIONSDF
MYARRAY dWORD 10, 20, 30
  MOV EAX, MYARRAY //GET 10
  MOV EAX, MYARRAY+1 //GET 20
  MOV EAX, [MYARRAY+1] //GET 20, USE THIS FOR CODE CLARITY WHILE USING ARRAY

## Slide 8: I KNOW ASSEMBLY!

## Slide 9: DEMO
DATA TRANSFERS – PART 1
https://github.com/shankar-ray/Assembly-Language-Tutorials-for-Windows/blob/master/04%20Data%20Transfers/Data%20Transfers%20-%20Part%201/Data%20Transfers%20-%20Part%201/Source.asm