## Slide 1: x86 CPU ARCHITECTURE
Sangram Kesari Ray <SHANKAR.RAY030@GMAIL.COM>

## Slide 2: CPU DESIGN
Clock //synchronization for operations – reading from memory, doing arithmetic in alu, etc.
Control unit
Arithmetic logic unit
BUS (parallel wires across the components, etched on the motherboard //between CPU and memory, etc.)
Instruction execution:
Fetch (instruction from memory ->
Decode (from binary bit pattern) ->
execute (update flags) ->
store (if any output operand)

## Slide 3: PROGRAM EXECUTION
Os loads a program into memory
Os executes the program’s first instruction (Entry Point)
From here The program runs by itself
When the program ends the os removes it from memory

## Slide 4: CPU OPERATION MODES
Protected mode //no direct access to system memory, each program has 2 gb address space
Real-address mode //direct access to system memory, each program has 1 mb address space
Virtual-8086 mode //CPU switching from protected to real mode
System management mode //used by system firmware

## Slide 5: REGISTERS
General purpose registers –
eax //accumulator register- holds data
ecx //counter register- loop counter
edx //data register- holds data
ebx //base register- pointer to data
esi //source index- pointer to source stream
edi //destination index- pointer to destination stream
ebp //base pointer- pointer to base of the stack
esp //stack pointer- pointer to top of the stack

## Slide 6: CONT.
Segment registers–
cs //code segment-pointer to starting address of program
ds //data segment-pointer to starting address of program data
ss //stack segment-defines stack area
es //extra segment-pointer to destination
fs //general purpose segment register
gs //general purpose segment register

## Slide 7: INSTRUCTION POINTER
EIP //POINTER TO NEXT INSTRUCTION
Note: system security is all about controlling the eip register – directly/in-directly to cause abnormal code execution.

## Slide 8: EFLAGS
A 32-bit register stores results of a certain operation in the cpu
0-bit //carry flag-if an arithmetic operation caused carry/borrow
2-bit //parity flag-set if number of bits in lsb is even
4-bit //adjust flag-if a carry occurs from lower nibble
6-bit //zero flag-set if result of an operation is zero
7-bit //sign flag-set if result of an operation is negative
8-bit //trap flag-set if step-by-step debugging

## Slide 9: CONT.
9-bit //interruption flag-set if interrupts are enabled
10-bit //direction flag-if set reading memory backwards
11-bit //overflow flag-if an output is larger for a register to hold
12-13-bit //i/o privilege level fields-i/o privilege level of current process
14-bit //nested task flag-set if current process is linked to the next process
16-bit //resume flag-if set, respond to debug exceptions
17-bit //virtual-8086 mode-set if in 8086 compabitibility mode
18-bit //alignment-flag-set if cpu detects an un-aligned memory operand, storing a word in an odd-byte address

## Slide 10: CONT.
19-bit //virtual interrupt flag- set after handling a pending interrupt
20-bit //virtual interrupt pending flag- set if an interrupt is pending
21-bit //identification flag-if set, cpu support cupid instruction
All other bits are reserved for cpu

## Slide 11: MMX REGISTERS
8 64-bit registers //they are like general purpose registers
MM0, MM1, MM2, MM3, MM4, MM5, MM6, MM7

## Slide 12: XMM REGISTERS
8 128-bit registers //they are like general purpose registers
XMM0, XMM1, XMM2, XMM3, XMM4, XMM5, XMM6, XMM7

## Slide 13: FLOATING-POINT UNIT
TO BE USED FOR FLOATING-POINT ARITHMETIC
8 80-bit DATA-REGISTERS- ST0, ST1, ST2, ST3, ST4, ST5, ST6, ST7
2 48-bit pointer registers-
fip (fpu instruction pointer),
fsC (FPU DATa pointer)
3 16-bit control registers-
ftag (tag register)
fctrl (control register)
fstat (status regiter)
1 11-bit opcode register //stores opcode of the last non-control instruction, like addition, etc

## Slide 14: X86-64 BIT PROCESSORS
64-bit long addresses
Currently only lower 48-bits are used
Has two modes – compatibility mode to run 16/32-bit operands and 64-bit mode to run 64-bit operands
16 64-bit general purpose register- rax, rbx, rcx, rdx, rdi, rsi, rbp, rsp, r8-r15
64-bit rflags register //upper 32-bits are not used, flags work same as 32-bit

## Slide 15: HOW COMPUTER WORKS
Q > I encourage the reading to figure out how typing something in notepad actually gets displayed on the screen?
BRAVE ARE THOSE WHO COULD MAKE IT THIS FAR! Next time when we meet, we’ll start with Assembly programming using Visual Studio and MASM Assembler. Bye!
HARDWARE
APPLICATION
OS
BIOS