## Slide 1: ASSEMBLY LANGUAGE FUNDAMENTALS
Sangram Kesari Ray <SHANKAR.RAY030@GMAIL.COM>

## Slide 2: INTEGER LITERALS/CONSTANTS
Different types of representations
  10 //decimal
  10d //decimal
  10b //binary
  10q //octal
  10o //octal
  10h //hexadecimal
  0a10h //hexadecimal, a hexadecimal literal beginning with a letter must have a leading 0

## Slide 3: Arithmetic Operators Precedence
3. Modulus MOD
1. Parentheses ()
2. Unary plus, minus +, -
3. Multiply, Divide *, /
4. Add, Subtract +, -

## Slide 4: REAL NUMBER/FLOATING POINT
IEEE 32-BIT FORMAT
  1-BIT //SIGN BIT
  8-BIT //EXPONENT
  23-BIT //MANTISSA
WRITTEN IN PROGRAM AS //[sign]integer.[integer][exponent]
  12.
  -10.1
  -3.
  +15.8
As data is stored as binary in the memory, we use 32-bit IEEE format
  12.375D is stored as 01000001010001100000000000000000B

## Slide 5: HOW THE HECK 12.375D is stored as 01000001010001100000000000000000B !
STEP 1
TAKE OUT THE INTEGER PART INTO BINARY //12D -> 1100B
ALGORITHM
TMP = FRACTIONAL PART //.375
TMP *= 2 //0.750 // TAKE OUT THE INTEGRAL PART FROM TMP => 0
WHILE TMP = ZERO // DO ABOVE
// 2*0.750 = 1.500 => TAKE OUT 1
// 2*0.500 = 1.000 => TAKE OUT 1
STEP 2
12.375D BECOME 1100.011B //
Step 3
IEEE REPRESENTATION OF 1100.011B IS 1.100011B x 23
EXPONENT 3 BECOMES 3+127(8-BIT SIGNED) = 130D = 10000010B //8-BIT
MANTISSA 100011B BECOMES 10001100000000000000000B //23-BIT
SIGN-BIT //1-BIT
01000001010001100000000000000000B // SIGN-BIT + EXPONENT + MANTISSA

## Slide 6: WTF!

## Slide 7: CHARACTER LITERALS/CONSTANTS
INSIDE SINGLE/DOUBLE QUOTS AS A, B, C, ETC.
STORED AS BINARY IN THE MEMORY
STRING LITERALS/CONSTANTS
SEQUENCE OF CHARACTER LITERALS

## Slide 8: IDENTIFIERS
IT CAN BE A VARIALBLE, A CONSTANT, A PROCEDURE OR A LABEL
DIRECTIVES
THEY ARE LIKE COMMANDS TO THE ASSEMBLER
  var1 BYTE 127 //this reserves space of 1-BYTE for var1
  .data //program segment/section to define variables
  .code //program segment containing instructions

## Slide 9: INSTRUCTIONS
BASIC FORMAT - [label:] mnemonic [operands] [;comment] // ANYTHING INSIDE SQUARE BRACKETS IS OPTIONAL
LETS SEE SOME SAMPLE INSTRUCTIONS WITH 0, 1, 2 AND 3 OPERANDS
  STC //SET CARRY FLAG
  INC EAX //INCREMENT EAX BY 1
  MOV EAX, 5 //STORE 5 IN EAX REGISTER
  IMUL EAX, EBX, 5 //MULTIPLY EBX BY 5 AND STORE IN EAX REGISTER

## Slide 10: Assembling, Linking and Running
1. Source file
2. Assembler
3. Linker
4. Loader
Write the program as source file
Assembler creates and object file out of the source file
Linker copies the procedures from link libraries and combines then with object file and crates an executable file
Loader reads the executable file into memory and redirects the CPU to program’s starting address

## Slide 11: DEFINITING DATA
The following directives allocate the corresponding space to the identifier/variables
  VAR1 BYTE 10 //ALLOCATE 8-BIT
  VAR2 SBYTE 10 //8-BIT SIGNED
  VAR3 WORD 10 //16-BIT
  VAR4 SWORD 10 //16-BIT SIGNED
  VAR5 DWORD 10 //32-BIT
  VAR6 SDWORD //32-BIT SIGNED
  VAR7 FWORD //48-BIT FAR POINTER
  VAR8 QWORD //64-BIT
  VAR9 TBYTE //80-BIT
  VAR10 REAL4 //32-BIT IEEE SHORT REAL (1-BIT SIGNED + 8-BIT EXPONENT + 32-BIT MANTISSA)
  VAR11 REAL8 //64-BIT IEEE LONG REAL (1-BIT SIGNED + 11-BIT EXPONENT + 52-BIT MANTISSA)
  VAR12 REAL10 //80-BIT IEEE EXTENDED REAL (1-BIT SIGNED + 15-BIT EXPONENT + 1-BIT INTEGER + 63-BIT MANTISSA)
  VAR13 DB //8-BIT
  VAR14 DW //16-BIT
  VAR15 DD //32-BIT OR REAL
  VAR16 DQ //64-BIT OR REAL
  VAR17 DT //80-BIT