## Slide 1: ASSEMBLY LANGUAGE FUNDAMENTALS
Sangram Kesari Ray <SHANKAR.RAY030@GMAIL.COM>

## Slide 2: INTEGER LITERALS/CONSTANTS
Different types of representations
  10 //decimal
  10d //decimal
  10b //binary
  10q //octal
  10o //octal
  10h //hexadecimal
  0a10h //hexadecimal, a hexadecimal literal beginning with a letter must have a leading 0

## Slide 3: Arithmetic Operators Precedence
3. Modulus MOD
1. Parentheses ()
2. Unary plus, minus +, -
3. Multiply, Divide *, /
4. Add, Subtract +, -

## Slide 4: REAL NUMBER/FLOATING POINT
IEEE 32-BIT FORMAT
  1-BIT //SIGN BIT
  8-BIT //EXPONENT
  23-BIT //MANTISSA
WRITTEN IN PROGRAM AS //[sign]integer.[integer][exponent]
  12.
  -10.1
  -3.
  +15.8
As data is stored as binary in the memory, we use 32-bit IEEE format
  12.375D is stored as 01000001010001100000000000000000B

## Slide 5: HOW THE HECK 12.375D is stored as 01000001010001100000000000000000B !
STEP 1
TAKE OUT THE INTEGER PART INTO BINARY //12D -> 1100B
ALGORITHM
TMP = FRACTIONAL PART //.375
TMP *= 2 //0.750 // TAKE OUT THE INTEGRAL PART FROM TMP => 0
WHILE TMP = ZERO // DO ABOVE
// 2*0.750 = 1.500 => TAKE OUT 1
// 2*0.500 = 1.000 => TAKE OUT 1
STEP 2
12.375D BECOME 1100.011B //
Step 3
IEEE REPRESENTATION OF 1100.011B IS 1.100011B x 23
EXPONENT 3 BECOMES 3+127(8-BIT SIGNED) = 130D = 10000010B //8-BIT
MANTISSA 100011B BECOMES 10001100000000000000000B //23-BIT
SIGN-BIT //1-BIT
01000001010001100000000000000000B // SIGN-BIT + EXPONENT + MANTISSA

## Slide 6: WTF!

## Slide 7: CHARACTER LITERALS/CONSTANTS
INSIDE SINGLE/DOUBLE QUOTS AS A, B, C, ETC.
STORED AS BINARY IN THE MEMORY
STRING LITERALS/CONSTANTS
SEQUENCE OF CHARACTER LITERALS

## Slide 8: IDENTIFIERS
IT CAN BE A VARIALBLE, A CONSTANT, A PROCEDURE OR A LABEL
DIRECTIVES
THEY ARE LIKE COMMANDS TO THE ASSEMBLER
  var1 BYTE 127 //this reserves space of 1-BYTE for var1
  .data //program segment/section to define variables
  .data? //segment contains un-initialized data
  .code //segment containing instructions

## Slide 9: INSTRUCTIONS
BASIC FORMAT - [label:] mnemonic [operands] [;comment] // ANYTHING INSIDE SQUARE BRACKETS IS OPTIONAL
LETS SEE SOME SAMPLE INSTRUCTIONS WITH 0, 1, 2 AND 3 OPERANDS
  STC //SET CARRY FLAG
  INC EAX //INCREMENT EAX BY 1
  MOV EAX, 5 //STORE 5 IN EAX REGISTER
  IMUL EAX, EBX, 5 //MULTIPLY EBX BY 5 AND STORE IN EAX REGISTER

## Slide 10: Assembling, Linking and Running
1. Source file
2. Assembler
3. Linker
4. Loader
Write the program as source file
Assembler creates and object file out of the source file
Linker copies the procedures from link libraries and combines then with object file and crates an executable file
Loader reads the executable file into memory and redirects the CPU to program’s starting address

## Slide 11: DEFINITING DATA
The following directives allocate the corresponding space to the identifier/variables
  VAR1 BYTE 10 //ALLOCATE 8-BIT
  VAR2 SBYTE 10 //8-BIT SIGNED
  VAR3 WORD 10 //16-BIT
  VAR4 SWORD 10 //16-BIT SIGNED
  VAR5 DWORD 10 //32-BIT
  VAR6 SDWORD //32-BIT SIGNED
  VAR7 FWORD //48-BIT FAR POINTER
  VAR8 QWORD //64-BIT
  VAR9 TBYTE //80-BIT
  VAR10 REAL4 //32-BIT IEEE SHORT REAL (1-BIT SIGNED + 8-BIT EXPONENT + 32-BIT MANTISSA)
  VAR11 REAL8 //64-BIT IEEE LONG REAL (1-BIT SIGNED + 11-BIT EXPONENT + 52-BIT MANTISSA)
  VAR12 REAL10 //80-BIT IEEE EXTENDED REAL (1-BIT SIGNED + 15-BIT EXPONENT + 1-BIT INTEGER + 63-BIT MANTISSA)
  VAR13 DB //8-BIT
  VAR14 DW //16-BIT
  VAR15 DD //32-BIT OR REAL
  VAR16 DQ //64-BIT OR REAL
  VAR17 DT //80-BIT

## Slide 12: BYTE AND FRIENDS
Single Initializer
VAR1 BYTE 10 //ALLOCATE 8-BIT
VAR2 SBYTE 10 //8-BIT SIGNED
VAR3 BYTE ? //UN-INITIALIZED, TO-BE ASSIGNED AT RUN-TIME
VAR4 DB 10 //OLD-SCHOOL
VAR5 BYTE “Hello-world”,0 //A NULL terminated string with double-quotes
VAR6 BYTE ‘Bye-world”,0 //Another NULL terminal string with single-quotes
Multiple Initializers
myArray BYTE 10, 11, 12 //1-D Array
myMatrix SBYTE 20, 21, 22 //2-D Matrix
BYTE 23, 24, 25
SBYTE 26, 27, 28
myArray2 BYTE 10 DUP (0) //allocates 10-BYTES and set all bytes to zero
myArray3 BYTE 10 DUP (?) //allocates 10-BYTES, un-initialized

## Slide 13: WORD AND FRIENDS
Single Initializer
VAR1 WORD 10 //ALLOCATE 16-BIT
VAR2 SWORD 10 //16-BIT SIGNED
VAR3 WORD ? //UN-INITIALIZED, TO-BE ASSIGNED AT RUN-TIME
VAR4 DW 10 //OLD-SCHOOL
Multiple Initializers
myArray WORD 10, 11, 12 //1-D Array
myMatrix SWORD 20, 21, 22 //2-D Matrix
WORD 23, 24, 25
SWORD 26, 27, 28
myArray2 WORD 10 DUP (0) //allocates 10-WORDS and set all WORDs to zero
myArray3 WORD 10 DUP (?) //allocates 10-WORDS, un-initialized

## Slide 14: DWORD AND FRIENDS
Single Initializer
VAR1 DWORD 10 //ALLOCATE 32-BIT
VAR2 SDWORD 10 //32-BIT SIGNED
VAR3 DWORD ? //UN-INITIALIZED, TO-BE ASSIGNED AT RUN-TIME
VAR4 DD 10 //OLD-SCHOOL
Multiple Initializers
myArray DWORD 10, 11, 12 //1-D Array
myMatrix SDWORD 20, 21, 22 //2-D Matrix
DWORD 23, 24, 25
SDWORD 26, 27, 28
myArray2 DWORD 10 DUP (0) //allocates 10-DWORDS and set all DWORDs to zero
myArray3 DWORD 10 DUP (?) //allocates 10-DWORDS, un-initialized

## Slide 15: QWORD AND FRIENDS
Single Initializer
VAR1 QWORD 10 //ALLOCATE 64-BIT
VAR2 QWORD ? //UN-INITIALIZED, TO-BE ASSIGNED AT RUN-TIME
VAR3 DQ 10 //OLD-SCHOOL
Multiple Initializers
myArray QWORD 10, 11, 12 //1-D Array
myMatrix QWORD 20, 21, 22 //2-D Matrix
QWORD 23, 24, 25
QWORD 26, 27, 28
myArray2 QWORD 10 DUP (0) //allocates 10-QWORDS and set all QWORDs to zero
myArray3 QWORD 10 DUP (?) //allocates 10-QWORDS, un-initialized

## Slide 16: TBYTE/PACKED BCD(BINARY CODED DECIMAL)
10-BYTES or 80-BIT //size
each half-byte of lower 9-bytes contains a single decimal digit
the highest bit of the highest byte contains sign-bit 0/1 (+/-)
lower 7-bits of the highest bytes are not used
+999999999999999999 //18-digits, max value
-999999999999999999 //18-digits, min value
I encourage the reader to figure out how BCD can be used in LED-display.

## Slide 17: REAL FRIENDS
Single Initializer
VAR1 REAL4 1.0 //4-BYTE
VAR2 DD 1.0 //4-BYTE
VAR3 REAL8 ? //8-BYTE
VAR4 DQ ? //8-BYTE
VAR5 REAL10 1.0 //10-BYTE
VAR6 DT 1.0 //10-BYTE
Multiple Initializers
myArray REAL4 1.0, 1.1, 1.2 //1-D Array
myMatrix REAL4 2.0, 2.1, 2.2 //2-D Matrix
REAL8 2.3, 2.4, 2.5
REAL10 2.6, 2.7, 2.8
myArray2 REAL4 1.0 DUP (0) //allocates 10-REAL4 and set all REAL4 to zero
myArray3 REAL4 1.0 DUP (?) //allocates 10-REAL4, un-initialized

## Slide 18: LITTLE-ENDIAN VS BIG-ENDIAN
  CPU STORES/RETRIEVE LEAST SIGNIFICANT BYTE FIRST //LITTLE
  CPU STORES /RETRIEVE THE MOST SIGNIFICANT BYTE FIRST //BIG

## Slide 19: SYMBOLIC CONSTANTS
They are associating an identifier with an integer, text, etc.
e.g.
mov eax, 10 //no symbolic constant
tmp = 10
mov eax, tmp //using symbolic constant
Symbolic constants allows more maintainable programs, like storing value of PI = 3.14

## Slide 20: CONT.
Using Assembler defined Symbolic constants: $, EQU and TEXTEQU
Finding string length
tmp = "Hello-world"
tmpLen = ($ - tmp)
Defining symbols as constants throughout the program //no re-definition allowed
PI EQU <3.14>
Creating textmacro //tiny code-chunks
addTenEAX TEXTEQU <add eax, 10>
Both these .code segments are same
.code
add eax, 10
.code
addTenEAX

## Slide 21: DEMO
Even-odd
https://github.com/shankar-ray/Assembly-Language-Tutorials-for-Windows/tree/master/03%20Assembly%20Language